## Slide 1
Bipolar Transistor (BJT)
Circuit Structure and Physical Properties
BJT Working Region
BJT Biasing Circuits
Current mirrors

## Slide 2
NPN and PNP bipolar transistor structure circuit diagram

## Slide 3
Bipolar transistors can have two different structures, NPN and PNP.
Their working principles are the same.
In NPN transistors, current carriers are electrons. So these transistors are faster.
Bipolar Transistör

## Slide 4
Bipolar Transistör
The bipolar transistor can be thought of as two diodes connected in the opposite direction.
In the normal operation of the bipolar transistor, the base-emitter junction is forward biased.
The base-collector junction is reverse biased.

## Slide 5
Transistor Working Principle
Doping concentration of the emitter, base and collector regions are different.
The most doping region is the emitter region.(N≈1019).
The base region is less doped (N≈1017) and the collector region is least doped (N≈1015).
Base region width should be shorter than L diffusion length.
a) Structure of bipolar transistor b) carrier density c) circuit diagram

## Slide 6
The electrons that pass into the base region are minority carriers here and begin to merge with the holes, which are the majority carriers here, and their number decreases as they move towards the collector side.
However, since the base region width is very short and the hole density in the base region is too low than the electron density in the emitter, most of the electrons entering the base region manage to arrive at the collector junction.
The electrons that reach here are rapidly attracted towards the collector side by the electric field created by the positive potential in the collector and they form the collector current by joining the electrons that are the majority carrier here.
Transistor Working Principle

## Slide 7
The emitter current is approximately equal to the collector current since most of the carriers passing from the emitter to the base region reach the collector region.
The few electrons are combined with holes in the base constitutes the base current. In this case, the base current is too small compared to the collector current.
On the other hand, the collector current is directly proportional to this small base current and the base current controls the collector current.
Transistor Working Principle

## Slide 8
Calculation of Base and Collector Currents

## Slide 9
Calculation of Base and Collector Currents
If the base region (WB) is larger than the Ln diffusion length, all electrons entering the base region combine with the holes and disappear. Hence, the collector current becomes zero. On the other hand, WB << Ln, very few electrons coming from diffusion combine with holes and 98% to 99.8% of these (this amount depends on base region doping concentration and WB / Ln ratio) creates collector current.
Electrons combined with holes in the base region also form the base current..
In this case, the following relations can be written.
IE = IB+IC
IC = IE − IB =αFIE ≈ IE

## Slide 10
Since IB << IE, the αF coefficient (current gain from emitter to collector) in this equation is less than one but very close to one and its value varies between 0,980… 0,998.
  IE = IB+IC If the value of the base current is calculated from its equation, the relation between the collector current and the base current is found below:
Calculation of Base and Collector Currents

## Slide 11: Bipolar Junction Transistors: Operation Modes
Bias Mode | E-B Junction | C-B Junction
Saturation | Forward | Forward
Active | Forward | Reverse
Cutoff | Reverse | Reverse
Saturation : In this method both the junctions are forward biased. This method is not useful as the transistor is in “saturation” and the current cannot be controlled easily.
Cutoff: In this method both the junctions are reverse biased. This method is also not useful as the transistor is in “cut-off” state since current is zero.
Active: This is the most common and popular method used in transistor biasing. In this method, the base-emitter junction is forward biased and collector-base junction is reverse biased. So by adjusting base voltage we can control total current in the transistor easily.
Operational modes are defined based on VBE and VBC

## Slide 12
BJT Operating Regions and I V Curves
Input characteristics
  the input takes the form of a forward-biased pn junction
  the input characteristics are similar to a semiconductor diode
Output characteristics
  region near to the origin is the saturation region
  this is normally avoided in linear circuits

## Slide 13: Input-Output Characteristics of BJT
Output Characteristic
Input Characteristic

## Slide 14
Operation Mode: vBE forward biased & vBC reversed biased (Aktif mod)
Shockley equation
IES=saturation current (10-12-10-16A); VT=kT/q -termal voltage (26mV)
Kirchhoff Law
Current Gain
BJTs – Current & Voltage Relations

## Slide 15
  The relationship between collector and base currents
  The characteristic is almost linear.
  Generally, the value of the collector current is much higher than the base current.
  The transistor provides current gain.

## Slide 16
BJT Load line analysis
Loop equation
For iB=0
For vBE=0
vBB
VBB/RB

## Slide 17
BJT Load line analysis
Loop Equation

## Slide 18
Sample : Find the IC and VC values by analyzing the circuit given below (a). For transistor in active region β = 100 and |VBE| = 0.7V . (RC = 5kΩ, RE = 7.07kΩ)
Notes: sedr42021_0515a.jpg

## Slide 19
Sample :
Find the IC and VE values by analyzing the circuit given below (a). For transistor in active region β = 100 and |VBE| = 0.7V .
Notes: sedr42021_0515a.jpg

## Slide 20
Transistor Working in Cutoff
In both junctions, it is reverse b
<
The transistor is in the cut and the current does not flow.

## Slide 21
Transistor Saturation Operation
Both junctions are forward biased
Transistör operates in saturation mode
= is baundary condition

## Slide 22
DC bias circuits for BJT
Identification and analysis of the operation of various biaising circuits:
Base bias circuits
Bias circuits with voltage divider
Emitter bias circuits
Bias circuits with Collector feedback
Bias circuits with emitter feedback

## Slide 23
DC Bias circuits for BJT

## Slide 24: BIAS CIRCUITS
1. (sabit kutuplama), FİXED BİAS CİRCUİT).

## Slide 29: Sample
Draw the DC load line for the circuit in the figure and mark the working point (Q). Determine if the circuit is biased at the midpoint.

## Slide 30: Sample
Circuşt is biased at the midpoint

## Slide 31: (shift of the working point)
In the circuit shown, the transistor has hFE = 100 for T = 25 ° C and hFE = 150 for T = 100 ° C. Determine the operating point IC and VCE values for both temperature values. VBE = 0.7V
Temp(°C) | IB (mA) | IC (mA) | VCE (V)
25 | 20.28 | 2.028 | 3.94
100 | 20.28 | 3.04 | 1.92
(250C)
Q(1000C)

## Slide 32: Base bias characteristics.
Advantage: the circuit is simple.
Disadvantage: Working point depends on temperature changes.
Applications: Switching circuits.
Circuit recognition: Single resistance (RB) between power supply (VCC) and base. There is no resistance in the emitter.

## Slide 33: Base bias characteristics.
Maksimum Ic current
Operating point equations:
Load line equations:

## Slide 34
2. (Gerilim bölücülü kutuplama)Voltage divider bias circuit.
1. Step: The circuit is rearranged so that all capacities are open circuit:

## Slide 35: 2. Gerilim bölücülü kutuplama (Voltage divider bias circuit).

## Slide 39: Stability of the voltage divider bias circuit
In the bias circuit with voltage divider, the hFE dependence of the operating point is less than that of the base bias circuit.
For example, IE 10 mA , hFE changes between 100 and 300
As can be seen, despite the great change of hFE, ICQ changes little.

## Slide 40: the voltage divider bias circuit characteristics.
Circuit recognition: Voltage divider in the base circuit.
Advantages: The working point of the circuit is not sensitive to hFE changes (stable).
Disadvantages: It needs more elements than most biased circuits.
Applications: It is primarily used to bias linear amplifiers.

## Slide 41: Sample
Find the value ICQ ve VCEQ.
ICQ @ IE (veya hFE >> 1) olduğundan,
|VBE| = 0.7V

## Slide 42: 3. Emmiter biasing.
Assuming the transistor operates in the active region;
For hFE >> 1,

## Slide 43: Line load for the emitter bias circuit

## Slide 44: Emitter biasing characteristics.
Circuit recognition: Symmetrical (positive and negative) supply source and base resistance is grounded.
Advantages:The working point of the circuit is not sensitive to hFE changes (stable).
Disadvantages:Needs symmetrical (positive and negative) supply source.
Apllications:It is primarily used to biase linear amplifiers.

## Slide 45: Emitter biasing characteristics.
Load line equations:
Working point equations :

## Slide 46: Sample
Find the value of ICQ ve VCEQ

## Slide 47: 4. Collector feedback bias

## Slide 48: Örnek
Find the value of ICQ ve VCEQ

## Slide 49: Stability of the collector feedback bias circuit
hFE increases
IC increases (IB at the same value)
VCE decrease
IB decrease
IC it doesn't increase much.
Stability is good. Sensitivity to hFE and temperature changes is low.

## Slide 50: Collector feedback bias characteristics
Circuit recognition: Base resistance connected between the base and the collector.
Advantages: Having a simple bias circuit with relatively stable operating point.
Disadvantages: Relatively weak (bad) AC characteristic
Applications: It is primarily used to bias linear amplifiers

## Slide 51
5. Emiter Geribeslemeli kutuplama (Emitter Stabilized Bias Circuit)

## Slide 56: 5. Emmiter stabilized bias circuit

## Slide 57: Sample

## Slide 58: Stability of the emitter stabilizied bias circuit
hFE artar
IC artar (IB aynı değerde iken)
VE artar
IB azalır
IC çok fazla artmaz.
Kararlılığı iyidir. IC değerinin hFE ve sıcaklık değişimlerine duyarlığı azdır.

## Slide 59: Emmiter stabilized bias circuit characteristics
Recognition of the circuit: It is similar to the voltage divider polarization circuit but R2 resistance is missing (or RE added base bias circuit).
Advantages: Having a simple biasing circuit with relatively stable operating point.
Disadvantages: It needs more elements than the collector feedback bias circuit.
Applications: It is primarily used to biaslinear amplifiers.

## Slide 60: Emmiter stabilized bias circuit characteristics
Working point equations:

## Slide 61
Increasing Biasing Stability

## Slide 62
a) BJT biased using a constant-current source IBIAS b) Circuit for implementation the current source IBIAS

## Slide 67
Find the value of β?