## Slide 1: INTRODUCTION to ELECTRONICS (10958)
Assoc. Prof. Dr. Hacer Atar Yıldız
E-mail: haceryildiz@itu.edu.tr
Room: 3104
Teaching Assistant:

## Slide 2: Course Weekly Lecture Plan
Weeks | Topics
1 | Introduction, overview of topics, overview of basic knowledge required for this course
2 | Atomic models, crystal structure, semiconductor physics, doping, current flow mechanisms, Continuity Equation
3 | pn junction, currents in unbiased pn junction, formation of depletion layer, carrier density diagrams, derivation of potential barrier and depletion layer thickness, and Semiconductor Diode Equation.
4 | Types of diodes, Zener effect, Zener diodes, diode capacities, sample circuits constructed with diodes
5 | Transistor physics, physical characteristics of BJT, biasing conditions, current components, transistor parameters
6 | BJT as a switch and biasing for analog applications
7 | Midterm Exam 1 (12 November 2024)
8 | Transistor amplifier circuits: equivalent AC circuits, small signal analysis
9 | Transistor amplifier circuits: gain and input/output resistance calculations, cascade amplifier circuits
10 | Differential amplifier circuits: configurations, gain and input/output resistance and CMRR calculations
11 | MOSFET, physical characteristics. MOS as a switch and biasing for analog applications
12 | Midterm Exam 2 (24 December 2024)
13 | Transistor amplifier circuits: MOS amplifiers
14 | Operational Amplifiers (OPAMP) and applications

## Slide 3: Grading
Midterm Exams 2x 30%, Final Exam 40%
To be eligible of taking the final, at least one mıdterm exam should be taken, with a minimum MIDTERM EXAM AVERAGE of 25/100..(the sum of your grades from MT exams should be 50/200 or more; i.e. {MT1+MT2} ≥ 50)
I created a Ninova page for your section. You can access it using your ITU student account and password.

## Slide 4: Textbooks
Microelectronic Circuits, A.S. Sedra, K.C. Smith, OxfordUniversity Press, 2003. ISBN: 0-19-514252-7.
Fundamentals of Microelectronics by Behzad Razavi (Author)
Elektronik Elemanları, D. Leblebici, SEÇ Yayın Dağıtım, Istanbul, 2001. ISBN: 975-7670-32-4.
Elektronik, M. Sait Türköz, Birsen Yayınevi, 2004, ISBN: 975-511-198-0;
Elektronik Devre Elemanları, Avni MORGÜL, PapatyaBilim, 2016.

## Slide 5
Introduction
Semiconductors & Doping, Basics of pn junction
Diodes
BJT Transistors
MOSFET Transistors
Operational Amplifiers
Introduction to Electronics

## Slide 6: Engineering Notation Scientific Units – positive powers
Power | Number | SI symbol | SI prefix
0 | 1 | (none) | (none)
3 | 1,000 | k | kilo
6 | 1,000,000 | M | mega
9 | 1,000,000,000 | G | giga
12 | 1,000,000,000,000 | T | tera
15 | 1,000,000,000,000,000 | P | peta

## Slide 7: Engineering Notation Scientific Units – negative powers
Power | Number | SI symbol | SI prefix
0 | 1 | (none) | (none)
−3 | 0.001 | m | milli
−6 | 0.000 001 | μ | micro
−9 | 0.000 000 001 | n | nano
−12 | 0.000 000 000 001 | p | pico
−15 | 0.000 000 000 000 001 | f | femto

## Slide 9: What is electronics?
The branch of engineering in which the flow and control of electrons in vacuum or semiconductor are studied is called electronics.
Electronics can also be defined as the branch of engineering in which the electronic devices and their utilization are studied.
Electronics have various branches include, digital electronics, analog electronics, micro electronics, nanoelectronics, optoelectronics, integrated circuit and semiconductor device.

## Slide 10: History of Electronic
Lee de Forest (August 26, 1873 – June 30, 1961) was an American inventor and scholar.
He made significant contributions to the science of electronic communications during the first three decades of the Twentieth Century. He held numerous patents on the technology of radio, television and film.
His most famous invention, in 1906, was the three-element "Audion" (triode) vacuum tube, the first practical amplification device.
Vacuum tubes played a major role in the field of microwave and high power transmission as well as television receivers.

## Slide 11
In 1947, Bell laboratories developed the first transistor based on the research of Shockley, Bardeen and Brattain.
In 1959, Jack Kilby of Texas Instruments developed the first integrated circuit.
Integrated circuits contain large number of semiconductor devices such as diodes and transistors in very small area.

## Slide 12
Basic Semiconductor Physics
  Semiconductors
  Intrinsic (undoped) silicon
  Doping
  Carrier concentrations

## Slide 13: What is Electricity?
Atoms contain
Protons (+)
Neutrons (0)
Electrons (-)
Protons are positively charged and electrons are negatively charged.
The unit of charge is Coulomb (C)

## Slide 14
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
-
electron motion
Current direction
Sign Convention for Current Flow
Electrons carry negative charge
Current flow is in opposite direction

## Slide 15: Current Flow
The direction of current flow is indicated by an arrow.
Note: The voltage sources in the circuit flow current through nodes and wires.
+
_
DC Voltage Source
Current flow is from a higher potential (voltage) to a lower potential (voltage).
higher potential

## Slide 16
Conducting wires
Electronic elements
If two or more nodes are connected just by wires, intersection point can be considered as one single node.
Electric Circuit
Group of nodes connected only by wires
One big node
One big node
A single node
Nodes are Connected
by Wires Only
Intersection point of wires is call as a node
+
_

## Slide 17
I1 = I2 + I3
Diagram b shows a mechanical analogy
From Conservation of Charge
The sum of charges flowing into a node must be equal to the sum of the charges flowing out of the node.
Current is the amount of electric charge (coulombs) flowing through a cross section of a conductor in one second

## Slide 18: Kirchhoff’s Current Law
The sum of currents flowing into a node must be balanced by the sum of currents flowing out of the node.
i1
i2
i3
node
i1 flows into the node
i2 flows out of the node
i3 flows out of the node
i1 = i2 + i3
Gustav Kirchoff was an 18th century German mathematician
+
_

## Slide 19
Voltage (Difference in energy level )
Voltages are measured across the nodes of a circuit.
The direction of a voltage is indicated by + and – signs.
+
_
+ v2 –
+
v3
–
+
v4
–
+
v1
–
higher potential
lower potential

## Slide 20: Kirchhoff’s Voltage Law
+
_
+ v2 –
+
v3
–
+
v4
–
+
v1
–
The voltage measured between any two nodes does not depend of the path taken.
voltage
Example of KVL:
v1= v2 + v3
Similarly:
v1= v2 + v4
voltage
and:
v3= v4
voltage

## Slide 21
This equation can also be written in the following form:
Kirchhoff’s Voltage Law: v1 = v2 + v3
–v1 + v2 + v3 = 0
A formal statement of Kirchhoff’s Voltage Law:
The sum of voltages around a closed loop is zero.
+
_
+ v2 –
+
v3
–
+
v4
–
+
v1
–

## Slide 22: Using the Formal Definition of KVL
+
_
+ v2 –
+
v3
–
+
v4
–
+
v1
–
Sum the voltages that are encountered around the loop.
Define an arrow direction around a closed loop.
If the arrow first encounters a plus sign, enter that voltage with a (+) into the KVL equation.
If the arrow first encounters a minus sign, enter that voltage with a (–) into the KVL equation.
For the inner loop :
–v1 + v2 + v3 = 0
“The sum of voltages around a closed loop is zero.”
–v4 – v2 + v1 = 0
For the outer loop:

## Slide 23
The Capacitor
Capacitors are one of the fundamental passive components. In its most basic form, it is composed of two conducting plates separated by a dielectric material.
The ability to store charge is the definition of capacitance.
Dielectric
Conductors

## Slide 24
Initially uncharged
capacitor

## Slide 25
Charging

## Slide 26
Fully charged
After fully charged, a capacitor behaves as an open circuit and does not allow current flow.

## Slide 27
Source removed
A capacitor with stored charge can act as a temporary battery.

## Slide 28: What is a Semiconductor?
Low resistivity => “conductor”
High resistivity => “insulator”
Intermediate resistivity => “semiconductor”
  conductivity lies between that of conductors and insulators
  generally crystalline in structure for IC devices
    In recent years, however, non-crystalline semiconductors have become commercially very important
polycrystalline amorphous crystalline

## Slide 29: Semiconductor Materials
Gallium
(Ga)
Phosphorus
(P)
Use the periodic table to find the number of valance electrons.
Group 4 = 4 Valance electrons

## Slide 30: Why is Silicon Used?
Silicon is a semiconductor.
Silicon’s electrical properties can be modified through a process called doping.
Silicon is also an abundant element on Earth.
The abundance of Si allows it to be extremely affordable and appealing

## Slide 31: Silicon
Silicon is element 14 in the Periodic Table
It has two electrons in its first shell, eight electrons in the second shell, and four electrons in the third shell.
Since the electrons in the third shell are the outermost electrons, silicon has four valence electrons.
  The valence electrons are the electrons that determine the most typical bonding patterns for an element.

## Slide 32: Conduction in Semiconductors
Semiconductors (Si) act as insulators at low temperatures and conductors at higher temperatures.
Conduction occurs at higher temperature because the electrons surrounding the semiconductor atoms can break away from their covalent bond and move freely about the lattice

## Slide 33: Semiconductor structure
A covalent bond consists of two atoms "sharing" a single electron.
Each atom forms 4 covalent bonds with the 4 surrounding atoms.
Therefore, between each atom and its 4 surrounding atoms, 8 electrons are being shared.

## Slide 34: Electronic Properties of Si
 There are 2 types of mobile charge-carriers in Si:
  Conduction electrons are negatively charged;
  Holes are positively charged.
 The concentration (#/cm3) of conduction electrons & holes in a semiconductor can be modulated in several ways:
    by adding special impurity atoms ( dopants )
    by applying an electric field
    by changing the temperature
    by irradiation

## Slide 35: Silicon
Atomic density: 5 x 1022 atoms/cm3
Si has four valence electrons. Therefore, it can form covalent bonds with four of its nearest neighbors.
When temperature goes up, electrons can become free to move about the Si lattice.

## Slide 36: Electron-Hole Pair Generation
When a conduction electron is thermally generated, a “hole” is also generated.
A hole is associated with a positive charge, and is free to move about the Si lattice as well.

## Slide 37: Semiconductor
Eg
conductive band
valence band
energy gap
metal
Semiconductor
Eg ~ 1~3 eV
insulation
doping
P-type (IIIA) (acceptor)
N-type (VA) (donor)
Energy band structure of different matters
energy band structure : metal, semiconductor, insulation
An intrinsic semiconductor, also called an undoped semiconductor, is a pure semiconductor without any significant dopant species present.
doping (extrinsic semiconductor ) : p-type, n-type

## Slide 38: Carrier Concentrations in Intrinsic Si
The “band-gap energy” Eg is the amount of energy needed to remove an electron from a covalent bond.
The concentration of conduction electrons in intrinsic silicon, ni, depends exponentially on Eg and the absolute temperature (T):

## Slide 39: Doping (N type)
Si can be “doped” with other elements to change its electrical properties.
For example, if Si is doped with phosphorus (P), each P atom can contribute a conduction electron, so that the Si lattice has more electrons than holes, i.e. it becomes “N type”:
Notation:
n = conduction electron
concentration

## Slide 40: Doping (P type)
If Si is doped with Boron (B), each B atom can contribute a hole, so that the Si lattice has more holes than electrons, i.e. it becomes “P type”:
Notation:
p = hole concentration

## Slide 41: Summary of Charge Carriers

## Slide 42: Electron and Hole Concentrations
Under thermal equilibrium conditions, the product of the conduction-electron density and the hole density is ALWAYS equal to the square of ni:
P-type material
N-type material

## Slide 43: Terminology
donor: impurity atom that increases n
acceptor: impurity atom that increases p
N-type material: contains more electrons than holes
P-type material: contains more holes than electrons
majority carrier: the most abundant carrier
minority carrier: the least abundant carrier
intrinsic semiconductor: n = p = ni
extrinsic semiconductor: doped semiconductor

## Slide 44: Summary
The band gap energy is the energy required to free an electron from a covalent bond.
  Eg for Si at 300K = 1.12eV
In a pure Si crystal, conduction electrons and holes are formed in pairs.
  Holes can be considered as positively charged mobile particles which exist inside a semiconductor.
  Both holes and electrons can conduct current.
Substitutional dopants in Si:
  Group-V elements (donors) contribute conduction electrons
  Group-III elements (acceptors) contribute holes
  Very low ionization energies (<50 meV)